## Slide 1: Common Units of Measure and Conversion Factors

## Slide 2
Area (Length x Width)
    SQI-square inches (in²)
    SQF-square feet (144 in²)
    MSI-thousand square inches (1000 in²)
    MSF-thousand square feet (144,000 in²)
    SYD-square yards (1,296 in²)
    SQM-square meter (1,550 in²)
    SQKM-square kilometer (1,550,000 in²)

## Slide 3
Weight
    LBS –pounds
    MLBS-thousand pounds
    Ton-two thousand pounds
    KG-kilogram (2.2 lbs)
    MT-Metric tonne (1000 kg)

## Slide 4
Basis Weight (Weight/Unit Area)
Common units:
    LBS/RM- Pounds per Ream
      36” x24” x500 ream basis
      3,000 SQ FT
      432,000 SQ IN
    GSM- Grams per Square Meter
    1 LB/RM= 1.63 GSM (i.e. 3.1 LB/RM= 5 GSM)
    1 GSM= 0.61 LB/RM (i.e. 5 GSM= 3.1 LB/RM)
Yield is the Inverse of basis weight (Sqi/Lb or M²/Kg)

## Slide 5
Basic Measures | Converting Weight to Area
To convert weight to area requires three pieces of information:
  Weight (lb)
  Basis Weight (lb/rm)
  Width (inches)
Basis Equation:
    Linear Feet=(Weight)/(Basis Weight*Width*12)
    Linear Yards=(Weight)/(Basis Weight*Width*36)
    Linear Meters=(Weight)/(Basis Weight*Width*39.37)

## Slide 6
Basic Measures | Converting Area to Weight
To convert area to weight requires three pieces of information:
  Area (Sqi)
  Basis Weight (lb/rm)
  Width (inches)
Basis Equation:
    Pounds=(Area*Basis Weight)/432,000
    Kilograms=(Area*Basis Weight)/950,400

## Slide 7
Basic Measures | Thickness (Caliper)
Thickness also referred to as caliper
Imperial (English) units
    Mil – .001” (one thousandth of an inch)
      Referred to as Gauge for film (100 GA= .001”)
      Referred to as Point for board (8 PT= .008”)
Metric units
    Micron – 25.4 Micron= 1 mil=.001”=.0254mm
      .000235” foil = 6um = .006mm